## Slide 1: FLUID MECHANICS CHAPTER- 2 / FLUID PROPERTIES
Al-Mansour University College
Civil Engineering Department
Second Year/ 2017-2018
Ahmed Layth, R.E., M.S.
الــمــحــاضــرة رقــم ( 2 )

## Slide 2
Density ( )
The density, also called mass density, of a fluid is its mass per unit volume.
Specific Weight ( )
Specific weight, also called unit weight, is the weight of a substance per unit volume.
Prove?
Specific weight varies since it g changes with altitude (
Specific Gravity ( )
Specific gravity is the ratio of the density
of a substance to the density of water at
specified temperature and pressure.
interesting
You weigh 6 times less on moon
than earth …. How?
g = 1.62 m/s2 on moon

## Slide 3
If it is not specified, use:
Prove?
SG of water = 1 … Why?
SG of mercury = 13.6 which means:
mercury is 13.6 dense than water at 25˚C
SG of blood = 1.05 at 4 ˚C and that means ..… ?
Example (1)
The speciﬁc gravity of vehicle gasoline is 0.74. Calculate the density and speciﬁc weight of the gasoline.
Note
SG is dimensionless

## Slide 4
Example (2)
A bottle is filled with a liquid. Total weight of the bottle and the liquid is 2 N, weight of the bottle is 0.2 N, and volume of the bottle is 1.5 litter. Find mass density, unit weight, and specific gravity of the liquid.

## Slide 5
Example (3)
15 kg of an oil with a density of 790 Kg/m3 is mixed with 10 kg of water. The volumes are additive, and the resulting mixture is homogenous. What is the specific gravity of the resulting mixture?

## Slide 6
Example (4)
A vessel contains 85 liter of water at 10°C and atmospheric pressure as shown in the figure below. If the water is heated to 70°C, what will be the
percentage change in its volume? What weight of water must be removed to maintain the volume at its original value? Water’s density at 10°C and 70°C is 999.7 kg/m3 and 977.8 kg/m3, respectively.

## Slide 8
Homework
Example (5)
A leak from a tap comes out in a separate drops instead of a stream. The main cause of this phenomenon is:
gravity.
air resistance.
viscosity.
surface tension.
none of these.
Example (6)
Prove that using SI and English units.
Example (7)
A vertical cylindrical tank with a diameter of 12 m and a depth of 4 m is filled to the top with water at 20 ⁰C. If the water is heated to 50 ⁰C, how much water will spill over in cubic feet? Water’s specific weight at 20°C and 50°C is 9.79 kN/m3 and 9.69 kN/m3, respectively. (Ans. 166 )