## Slide 1: FLUID MECHANICS CHAPTER- 2 / FLUID PROPERTIES
Al-Mansour University College
Civil Engineering Department
Second Year/ 2017-2018
Ahmed Layth, R.E., M.S.
الــمــحــاضــرة رقــم ( 3 )

## Slide 2
Viscosity (µ)
The viscosity, also called dynamic viscosity, is the resistance of liquid to flow.
The resistance to fluid flow is controlled by internal friction forces within the liquid.
Thus, viscosity is a measure of the consistency of a fluid and its inability to flow.
A high viscous fluid flows slowly.

## Slide 3
Viscosity of water at 20 ˚C is:
Viscosity affected by temperature. The table below shows viscosity of water at different temperatures.
Kinematic Viscosity (ν)
Kinematic viscosity is the ratio of dynamic viscosity to mass density.
Kinematic viscosity of water at 20 ˚C is:
Prove?
Note
Viscosity of a liquid decreases as temperature increases … Why?
Temperature, °C | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Viscosity, mPa·s | 1.3 | 1 | 0.8 | 0.65 | 0.55 | 0.46 | 0.4 | 0.35 | 0.31 | 0.28

## Slide 4
Surface Tension (σ)
Surface tension is known as a membrane that seems to form on the free surface of a fluid due to cohesion forces.
Molecular attraction of a liquid forms due to cohesion and adhesion forces.
Cohesion: water is attracted to water.
Adhesion: water is attracted to other substances.
interesting
1
Surface tension is the reason that insects are able to sit on a pond and a needle is able to float on the surface of a glass of water, even though both are denser than water supports them.

## Slide 5
The effect of surface tension is illustrated for the case of capillary action by inserting the end of a small diameter tube into a reservoir of water.
capillary tubes
Capillary
attraction
Capillary
repulsion
Water
Mercury
For water:
cohesion < adhesion
For mercury:
cohesion > adhesion