## Slide 1: FLUID MECHANICS CHAPTER- 3 / FLUID STATIC
Al-Mansour University College
Civil Engineering Department
Second Year/ 2017-2018
Ahmed Layth, R.E., M.S.
الــمــحــاضــرة رقــم ( 4 )

## Slide 2
Fluid Static
As mentioned before, fluid static is the study of fluids at rest (in equilibrium).
Pressure is defined as the ratio of normal force to area at a point.
1 bar = 100 kPa (SI units)
Fluid pressures are measured with respect to two pressure references: zero pressure and atmospheric pressure.
Pressures measured with respect to a true zero pressure reference (pressure in a perfect vacuum) are known as absolute pressures.
e.g., 25 kPa-abs
Pressures measured with respect to atmospheric pressure are known as gage pressures.
e.g., 25 kPa-gage

## Slide 3
Note
To distinguish absolute and gage pressures, a letter g is used, e.g.:
25 kPag  measured with respect to atmosphere.
25 kPa  measured with respect to zero absolute.
pressure at point A
pressure at B
From the figure, it can be concluded:
+
-
= 101.3 kPa
at sea level
Max = - 101.3 kPa

## Slide 4
Hydrostatic pressure
Hydrostatic pressure is the pressure a fluid exerts on an immersed object or on container walls.
Hydrostatic pressure in a stationary and incompressible fluids behaves according to the following characteristics:
a. Pressure at a point has the same magnitude in all directions (Pascal’s law).
b. Pressure is always normal to a surface, regardless of the surface’s shape or orientation.

## Slide 5
c. Pressure is independent of an object’s area and size, and of the weight or mass of water above the object. The figure below illustrates the hydrostatic paradox.
atmospheric pressure
h
Pressure is a function of vertical depth and density only.
Prove?
d. If density is constant, pressure will vary linearly with vertical depth.
interesting
As Patm = 101.3 kPa, there are 10.33 meters of water column above us.
…... How?

## Slide 6
Example (1)
Find pressure and absolute pressure at points A, B, C, and D for the figure below.
4 m
A
B
C
D
3 m
2 m
3.5 m
5 m

## Slide 7
Example (2)
Find pressure at points A, B, C, and D for the figure below neglecting air.

## Slide 8
Example (3)
An open tank contains 5.7 m of water covered with 2.8 m of kerosene (). Find the pressure at the interface and at the bottom of the tank.

## Slide 9
Example (4)
A vessel containing oil under pressure as shown in the figure below. Find the height of the oil-surface in the attached piezometer.

## Slide 10
Homework
Example (5)
Find the pressure at points A, B, C, and D for the figure below. Neglect air.
(Ans. PD = - 624 )

## Slide 11
Homework
Example (6)
The closed tank in the figure shown, if the pressure at point A is 98 kPa abs, what is the absolute pressure at point B? Use
(Ans. 78.28 kPa)

## Slide 12
Homework
Example (7)
The air-oil-water system shown in the figure below, if gage A reads 160 kPa abs and gage B reads 39 less than gage C, calculate:
The specific weight of the oil. ( Ans. 4.8 kN/)
2. The reading of gage C using . (Ans. 208.6 kPa)
3 m
3 m
2 m
2 m

## Slide 13
Homework
Example (8)
A pressure gage 7.0 m above the bottom of a tank containing a liquid reads 64.94 kPa; another gage at height 4.0 m reads 87.53 kPa. Calculate the specific weight and mass density of the fluid.
(Ans. 7.53 kN/ and 767.6 kg/, respectively)