## Slide 1: FLUID MECHANICS CHAPTER- 4 / FLUID Dynamic
Al-Mansour University College
Civil Engineering Department
Second Year/ 2017-2018
Ahmed Layth, R.E., M.S.
الــمــحــاضــرة رقــم ( 6 )

## Slide 2
Fluid Dynamics
Fluid dynamics is the study of fluids in motion.
Flow Rate
Mass-Volume flow rate relationship:
Prove?
Mass flow rate
It is the mass of fluid (m) flowing per unit time (t).
Symbol:
Equation:
Units: kg/s
Volume flow rate
It is the volume of fluid (V) flowing per unit time (t).
Symbol: Q
Equation: = A v
Units: /s

## Slide 3
Example (1)
A student took 15 seconds to collect water in a 0.5 kg bucket. The mass of bucket and water was 5 kg. What is the mass and volume flow rates?
Example (2)
What is the time required to fill 2 tank with water if the discharge is 0.01 ? At which discharge will the tank be empty after 30 seconds of its full volume?

## Slide 4
Continuity Equation
From conservation of mass and steady state flow (fluid properties are not function of time):
Example (3)
Water flows from 200 mm pipe to 100 mm pipe. If the velocity of flow is 2 m/s in the larger pipe, calculate the velocity in the smaller pipe, discharge, and mass flow rate.
Prove?

## Slide 5
Example (4)
Diameter of pipes 1, 2, and 3 is 50 mm, 40 mm, and 60 mm, respectively. Mean velocity of pipe 1 is 2 m/s. Pipe 2 takes 30% of total discharge. Calculate the discharge and velocity in each pipe.
1
2
3

## Slide 6
Example (5)
Assuming complete mixing occurs between the two inflows (A and B) before the mixture discharges from the pipe at C. Find the mass rate of flow, the velocity, and the specific gravity of the mixture in the pipe at C using the table below.
A
B
C
Pipe | d, cm | Q, | SG
A | 15 | 0.1 | 0.95
B | 10 | 0.02 | 0.85
C | 15 | ? | ?
Pipe | d, cm |  | SG
A | 15 | 0.1 | 0.95
B | 10 | 0.02 | 0.85
C | 15 | ? | ?

## Slide 7
Homework
Example (6)
Water flows steadily through the nozzle shown in the figure below. Pipe diameters are 220 mm and 80 mm, respectively. Calculate the average velocities at sections 1 and 2. mass flow rate is 60 kg/s.
(Ans. 1.58 m/s and 12 m/s, respectively)

## Slide 8
Homework
Example (7)
The velocity of flow through pipe 1 is 5 m/s for the figure shown. Calculate the velocity of flow through pipe 2 if the water level h is constant.
(Ans. 6.47 m/s)

## Slide 9
Homework
Example (8)
Pipes (1) and (2) shown in the figure are of diameters 3 cm and pipe (3) is 4 cm diameter. Oil (S.G. = 0.8) enters section 1 at 6 m/s while water enters section 2 at 10 m/s . Assuming ideal mixing of incompressible fluids, calculate the exit velocity and density of mixture at section 3.
(Ans. 9 m/s and 923 )