## Slide 1: Lecture 9
Soil Stabilization and Compaction
Asst. Lect. Ali Khalid

## Slide 2
Volumetric Measure: For bulk materials volumetric measure varies with the materials position in the construction process see figure below, the same weight of a material will occupy different volumes as the material is handling on the project.

## Slide 3
1 Cubic Yards
in natural conditions in-place Yards
(Bank Yards)
1.25 Cubic Yards after digging
(Loose Yards)
0.9 Cubic Yards
after compaction (Compacted Yards)

## Slide 4
Soil volume is measured in one of these states:-
Bank cubic yard or meter: one cubic yard or one cubic meter of material as it lies in the natural state ( Bcy or Bcm )
Loose cubic yard or meter: one cubic yard or one cubic meter of material after it has been distance by a loading process ( Lcy or LCm ).
Compacted cubic yard or meter: one cubic yard or one cubic meter of material in the compacted state ( Ccy , Ccm )

## Slide 5
In planning or estimating a job, the engineer must use a consistent volumetric state in any set of calculations. The necessary consistency volumetric of units can achieve by:
Shrinkage factor =
Shrinkage % =
Swell factor =
Swell % = ( ) * 100
C or C = B or B ( 1- sh % )
L or L = B or B ( 1+ sw % )

## Slide 6
Soil Compaction
Compaction can:
Reduce settlements.
Increase strength.
Improve bearing capacity.
Control volume changes.
Lower permeability.

## Slide 9
Tamping foot rollers:
Used for clays, mixtures of sand and clay.
Sheeps foot rollers:
Used for soil containing rocks
Smooth wheel rollers: Sand, gravel, crushed stone
Pneumatic tired rollers: sand, gravel and pavement surface
Vibrating Compactors: sand, gravel, rock

## Slide 10
Soil Stabilization
Soil stabilization is any treatment of soil which increases its natural strength, there are two kinds of stabilization:-
1-Mechaincal
2-Chemical
Methods of stabilization soils included, but are not limited to, the following operations:
Blending and mixing heterogeneous soils to produce more homogeneous soils.
Incorporating lime or lime-fly ash into soils that have high clay content.
Blending asphalt with the soil.
Incorporating Portland cement with soils they are largely granular in nature.
Incorporating various salts into the soil.
Incorporating certain chemicals into the soil.
compacting the soils after they are processed