## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2
IDEAL OPERATIONAL AMPLIFIER AND OP-AMP CIRCUITS
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 3
inverting
non-inverting
output
Open loop mode
Vo = Aod ( v2 – v1)
  Aod is referred to as the open loop gain.
  Notice that is v2 = v1, the open loop gain equals to 
Op-amp circuit symbol
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 4
Two main characteristics:
    We want the open loop gain to be equal to  which means that v2 = v1
    the input resistance to be equal to  , hence there is no current going into the op-amp
0
0
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 5
Op amp can be configured to be used for different type of circuit applications:
  Inverting Amplifier
  Non – inverting Amplifier
  Summing Amplifier
  Integrator
  Differentiator
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 6: Inverting Amplifier
Op-amp as an inverting amplifier
Voltage at node 1 (inverting) = voltage at node 2 (non-inverting ) KCL at node 1:
I1 – I2 – Iin = 0
(Vi – 0) / R1 = (0 – Vo) / R2
Vi / R1 = - Vo / R2
Vo = - R2
Vi R1
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 7: Example 1
Gain = - (R2 / R1) = -(150/12) = -12.5
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 8: Example 2
Answers:
- 6
- 0.27 V
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 9
Voltage Follower / Buffer Amplifier
vo = vI
Hence, gain = 1
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 10
Summing Amplifier
i1 + i2 + i3 – i4 – 0 = 0
Similarly,
Example 8.2
Design a summing amplifier as shown in figure to produce a specific output signal, such that vo = 1.25 – 2.5 cos t volt. Assume the input signals are vI1 = -1.0 V, vI2 = 0.5 cos t volt. Assume the feedback resistance RF = 10 k
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 11
Solution: output voltage
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College
Notes: <number>

## Slide 12: Other Op-Amp Applications
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 13
When the feedback resistor of an inverter circuit is replaced by a capacitor the circuit is worked as an integrator circuit -cause the output to respond to changes in the input voltage over time
Integrator
Integrator circuit
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College