## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2: Science, Measurements, Uncertainty and Error
Science, Measurement, Uncertainty and Error
<number>
Notes: Permission to use this images has not been granted yet.

## Slide 3: Measurement and Uncertainty
Science, Measurement, Uncertainty and Error
<number>
Most experiments require scientists to make measurements.
Measurements are rarely exactly the same.
Measurements are always somewhat different from the “true value.”
These deviations from the true value are called errors.

## Slide 4: Sources of Error
Science, Measurement, Uncertainty and Error
<number>
Two sources of error in a measurement are
  limitations in the sensitivity of the instruments
  imperfections in experimental design or measurement techniques
Errors are often classified as:
  Random
  Systematic
www.nabis.govt.nz

## Slide 5: Random Errors
Science, Measurement, Uncertainty and Error
<number>
ALWAYS present.
Measurements are often shown as:
Measurement ± Random Error
Sources:
  Operator errors
  Changes in experimental conditions
How to minimize them?
  Take repeated measurements and calculate their average.
Notes: Permission to use this image has not been granted yet.

## Slide 6: Systematic Errors
Science, Measurement, Uncertainty and Error
<number>
Sources:
  Instrumental, physical and human limitations.
    Example: Device is out-of calibration.
How to minimize them?
  Careful calibration.
  Best possible techniques.
Are TYPICALLY present.
Measurements are given as:
Measurement + Systematic Error
OR
Measurement - Systematic Error
Notes: Permission to use this image has not been granted yet.

## Slide 7: Precision and Accuracy in Measurements
Science, Measurement, Uncertainty and Error
<number>
Precision
How reproducible are measurements?
Accuracy
How close are the measurements to the true value.

## Slide 8: Dartboard analogy
Science, Measurement, Uncertainty and Error
<number>
Imagine a person throwing darts, trying to hit the bulls-eye.
Not accurate
Not precise
Accurate
Not precise
Not accurate
Precise
Accurate
Precise

## Slide 9: Precision of a Measurement
Science, Measurement, Uncertainty and Error
<number>
The last digit is an estimate.
The precision is limited by the instrument.
Measurement ≈ 26.13 cm

## Slide 10: Scientific Data
Science, Measurement, Uncertainty and Error
<number>
The precision and accuracy are limited by the instrumentation and data gathering techniques.
Scientists always want the most precise and accurate experimental data.

## Slide 11: Dealing with Errors
Science, Measurement, Uncertainty and Error
<number>
Identify the errors and their magnitude.
Try to reduce the magnitude of the error.
HOW?
  Better instruments
  Better experimental design
  Collect a lot of data

## Slide 12: Bad news…
Science, Measurement, Uncertainty and Error
<number>
No matter how good you are… there will always be errors.
The question is… How to deal with them?
STATISTICS