## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2
SI derived units
Other quantities, called derived quantities, are defined in terms of the seven base quantities via a system of quantity equations. The SI derived units for these derived quantities are obtained from these equations and the seven SI base units. For ease of understanding and convenience, 21 SI derived units have been given special names and symbols, as shown in Table. The special names and symbols of the 21 SI derived units with special names and symbols given in Table may themselves be included in the names and symbols of other SI derived units.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 3
Other not SI units
Bit: A bit is the smallest unit of data in a computer. A bit has a single binary value, either 0 or 1. Although computers usually provide instructions that can test and manipulate bits, they generally are designed to store data and execute instructions in bit multiples called bytes. In most computer systems, there are eight bits in a byte. The value of a bit is usually stored as either above or below a designated level of electrical charge in a single capacitor within a memory device. Half a byte (four bits) is called a nibble. In some systems, the term octet is used for an eight-bit unit instead of byte. In many systems, four eight-bit bytes or octets form a 32-bit word. In such systems, instruction lengths are sometimes expressed as full-word (32 bits in length) or half-word (16 bits in length).
Decibel (dB): One tenth of the common logarithm of the ratio of relative powers, equal to 0.1 B (bel). Note 1: The decibel is the conventional relative power ratio, rather than the bel, for expressing relative powers because the decibel is smaller and therefore more convenient than the bel. The ratio in dB is given by
dB = 10 log10(P1/P2)
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 4
Other not SI units
Neper (Np): A unit used to express ratios, such as gain, loss, and relative values. Note 1: The neper is analogous to the decibel, except that the Naperian base 2.718281828. . . is used in computing the ratio in nepers. Note 2: The value in nepers, Np , is given by Np = ln(x 1/x 2), where x 1 and x 2 are the values of interest, and ln is the natural logarithm, i.e., logarithm to the base e. Note 3: One neper (Np) = 8.686 dB, where 8.686 = 20/(ln 10). Note 4: The neper is often used to express voltage and current ratios, whereas the decibel is usually used to express power ratios. Note 5: Like the dB, the Np is a dimensionless unit. Note 6: The ITU recognizes both units.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College