## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2
Designing an ammeter
Galvanometer:
current flows through a coil in a magnetic field
coil experiences a torque, connected needle deflects
(see later chapters of this class)
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 3
Designing an ammeter
ammeter can be based on galvanometer
(for electronic instrument, use electronic sensor instead, analysis still applies)
simplest case: send current directly through galvanometer, observe deflection of needle
Needle deflection is proportional to current. Each galvanometer has a certain maximum current corresponding to full needle deflection.
What if you need to measure a larger current?
use shunt resistor
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 4
Ammeter uses a galvanometer and a shunt, connected in parallel:
A
I

Everything inside the green box is the ammeter.
Current I gets split into Ishunt and IG
Homework hint:
If your galvanometer reads 1A full scale but you want the ammeter to read 5A full scale, then RSHUNT must result in IG=1A when I=5A. What are ISHUNT and VSHUNT?
G
RG
RSHUNT
IG
ISHUNT
I
A
B
galvanometer
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 5
G
RG
RSHUNT
IG
ISHUNT
I
A
B
Shunt also reduces resistance of the ammeter:
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 6
A galvanometer-based ammeter uses a galvanometer and a shunt, connected in parallel:
G
RG
RS
IG
IS
I
Example: what shunt resistance is required for an ammeter to have a resistance of 10 m, if the galvanometer resistance is 60 ?
(actually 0.010002 )
To achieve such a small resistance, the shunt is probably a large-diameter wire or solid piece of metal.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 7
voltmeter must have a very large resistance
voltmeter can be made from galvanometer in series with a large resistance
V
G
RG
RSer

Everything inside the blue box is the voltmeter.
a
b
Vab
a
b
Vab
Homework hints: “the galvanometer reads 1A full scale” would mean a current of IG=1A would produce a full-scale deflection of the galvanometer needle.
If you want the voltmeter shown to read 10V full scale, then the selected RSer must result in IG=1A when Vab=10V.
Homework hints: “the galvanometer reads 1A full scale” would mean a current of IG=1A would produce a full-scale deflection of the galvanometer needle.
If you want the voltmeter shown to read 10V full scale, then the selected RSer must result in IG=1A when Vab=10V.
Designing a voltmeter
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 8
Ohmmeter measures resistance of isolated resistor
Ohmmeter can be made from a galvanometer, a series resistance, and a battery (active device).
G
RG
RSer
R=?
Terminals of ohmmeter are connected to unknown resistor
battery causes current to flow and galvanometer to deflect
V=I (Rser + RG + R) solve for unknown R

Measuring Instruments: Ohmmeter
Everything inside the blue box is the ohmmeter.
V
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College