## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2
Analogue and Digital waveforms measurements using an oscilloscope
<number>
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 3: Analog & Digital Signals
<number>
This presentation will
Review the definitions of analog and digital signals.
Detail the components of an analog signal.
Define logic levels.
Detail the components of a digital signal.
Review the function of the virtual oscilloscope.
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Introductory Slide / Overview of Presentation
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 4: Analog and Digital Signals
Analog Signals
Continuous
Infinite range of values
More exact values, but more difficult to work with
Digital Signals
Discrete
Finite range of values (2)
Not as exact as analog, but easier to work with
<number>
Example:
A digital thermostat in a room displays a temperature of 72. An analog thermometer measures the room temperature at 72.482. The analog value is continuous and more accurate, but the digital value is more than adequate for the application and significantly easier to process electronically.
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: This slide defines analog and digital signals and gives several examples of each.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 5: Example of Analog Signals
An analog signal can be any time-varying signal.
Minimum and maximum values can be either positive or negative.
They can be periodic (repeating) or non-periodic.
Sine waves and square waves are two common analog signals.
Note that this square wave is not a digital signal because its minimum value is negative.
<number>
0 volts
Sine Wave
Square Wave
(not digital)
Random-Periodic
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Examples of common analog signals.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 6: Parts of an Analog Signal
<number>
Amplitude
(peak-to-peak)
Amplitude
(peak)
Period
(T)
Frequency:
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Parts of an analog signal: amplitude, period, & frequency.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 7: Logic Levels
Before examining digital signals, we must define logic levels. A logic level is a voltage level that represents a defined digital state.
Logic HIGH: The higher of two voltages, typically 5 volts
Logic LOW: The lower of two voltages, typically 0 volts
<number>
5.0 v
2.0 v
0.8 v
0.0 v
Logic Low
Logic High
Invalid
Logic
Level
Logic Level | Voltage | True/False | On/Off | 0/1
HIGH | 5 volts | True | On | 1
LOW | 0 volts | False | Off | 0
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: This slide introduces the concept of logic levels, gives the range of acceptable voltages for a logic high & low, and lists other common terms used to describe logic levels.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 8: Example of Digital Signals
Digital signal are commonly referred to as square waves or clock signals.
Their minimum value must be 0 volts, and their maximum value must be 5 volts.
They can be periodic (repeating) or non-periodic.
The time the signal is high (tH) can vary anywhere from 1% of the period to 99% of the period.
<number>
0 volts
5 volts
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Examples of common digital signals.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 9: Parts of a Digital Signal
<number>
Amplitude
Time
High
(tH)
Time
Low
(tL)
Period (T)
Rising Edge
Falling Edge
Amplitude:
  For digital signals, this will ALWAYS be 5 volts.
Period:
  The time it takes for a periodic signal to repeat. (seconds)
Frequency:
  A measure of the number of occurrences of the signal per second. (Hertz, Hz)
Time High (tH):
  The time the signal is at 5 v.
Time Low (tL):
  The time the signal is at 0 v.
Duty Cycle:
  The ratio of tH to the total period (T).
  Rising Edge:
  A 0-to-1 transition of the signal.
Falling Edge:
  A 1-to-0 transition of the signal.
Frequency:
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: The parts of a digital signal: amplitude, period & frequency, time high, time low, duty cycle, rising & falling edge.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 10: Oscilloscope
The Oscilloscope is a piece of electronic test equipment that is used to capture and measure time-varying signals, both analog and digital.
Oscilloscopes can be found on the workbench (physical) as well as part of a simulation tool (virtual).
We will limit our usage to the virtual oscilloscope.
<number>
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 11: Virtual Oscilloscope: Multisim
<number>
Oscilloscope
Component
Oscilloscope Instrumentation
Timebase:
  Adjusts the time scale and offset of the signals. This is common for all channels.
Channel_X:
  Adjusts the horizontal scale and offset of the selected channel.
Channel Selection
Marker Display:
  Displays the voltage & time intersect for the markers T1 & T2.
Markers:
  Movable markers T1 & T2
Displayed Signals
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Review with the student Multisim Oscilloscope.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 12: Example: Digital Signal
Example:
  Determine the following information for the digital signal shown:
  Amplitude
  Period (T)
  Frequency (f)
  Time High (tH)
  Time Low (tL)
  Duty Cycle (DC)
<number>
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next two slides.
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 13: Example: Digital Signal
Solution:
  Amplitude:
  Period (T):
  Frequency (f):
<number>
2 ms / div
2 v / div
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Here is the solution. If you print handouts, do not print this page. (1 of 2)
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 14: Example: Digital Signal
Solution:
  Time High (tH):
  Time Low (tL):
  Duty Cycle (DC):
<number>
2 ms / div
2 v / div
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Here is the solution. If you print handouts, don’t print this page. (2 of 2)
Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 15: Period Measurement with Markers
The markers can be used to measure the period tH & tL (next slide).
<number>
  Period (T):
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 16: tH & tL Measurement with Markers
<number>
  Time High ( tH):
  Low High ( tL):
4 October 2018
By : Firas AL Assadi / AL Mansour University College
Notes: Analog and Digital Signals
Digital Electronics TM
1.2 Introduction to Analog
Project Lead The Way, Inc.
Copyright 2009
<number>