## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2: Main Oscilloscope Components
<number>
Vertical display controls Scales the input voltage to set the size and position of the waveform.
Horizontal display controls Sets the “sweep rate” (time / division) and adds a horizontal position control.
Trigger System and controls If the horizontal sweep begins randomly, the waveform moves around. The trigger stabilizes the waveform by controlling where, on a waveform’s voltage and slope, the display trace begins each time.
This scope also has a built-in signal generator.
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 3: The scope display
<number>
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 4: Vertical controls
<number>
Turn the channel display on & off (toggle the On button)
Set the vertical scale (press desired scale on Volts/Div.)
Set vertical position (slide bar)
Set input coupling (select buttons at bottom)
Set probe type (select buttons at bottom center)
  use 1x for the black coax probes from Electronix Express.
  use 1X or 10x for the probe supplied with Velleman scope
Autoset can be friend or foe!
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 5: Scope Input Coupling
<number>
Input coupling may be:
DC Coupling displays all of a signal, including any DC offset. True RMS measurement requires DC coupling.
AC coupling strips the DC component from a waveform, leaving only the time varying portion of the signal.
GND disconnects the input signal.
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 6: Horizontal controls
<number>
To the right of the waveform display area is the Time/Div. horizontal scale setting buttons.
The Run button enables the Horizontal display.
The single button is used to display a single horizontal capture.
Below the waveform display area is a slide bar to move the waveform sideways along the horizontal scale.
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 7: Trigger controls
<number>
Turn the trigger on and off (use the buttons). If the trigger is off, the display will free run.
If the trigger is on and you see Waiting for trigger… Select the trigger source (buttons) Select whether to trigger on rising edge or falling edge of the waveform. (buttons) Adjust the trigger voltage level (slide bar) until you see Running.
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 8: Trigger markers tell you what the trigger is doing.
<number>
There are markers on the edges of
the scope waveform display that
correspond to the waveform’s
trigger voltage level
trigger time (appears when you move the horizontal position slide bar to display the waveform before the trigger occurred)
4 October 2018
By : Firas AL Assadi / AL Mansour University College

## Slide 9: Visually measuring the waveform
<number>
On the scope display, Vmax, Vmin, Vpp, and period can be obtained by
counting the number of divisions
multiplying by the vertical scale for voltages
multiplying by the horizontal scale for time period.
4 October 2018
By : Firas AL Assadi / AL Mansour University College