## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2: Oscilloscope
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 3: Oscilloscope
Electron guns
Electron beams
Focusing coils
Deflection coils
Anode connection
Mask for separating beams for red, green, and blue part of displayed image
Phosphor layer with red, green, and blue zones
Close-up of the phosphor-coated inner side of the screen
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 4: Oscilloscope
Referred to as cathode-ray oscilloscope, it is a universal instrument that displays wave forms on a phosphor coated "screen" of a cathode-ray tube (CRT).
The oscilloscope represents a two dimensional graph of signals VS time or in general, other signals (instead of time).
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 5: oscilloscope
The general purpose of an oscilloscope is displaying voltage signals and other electrical signals or non-electrical signals.
There non-electrical signals would have to be converted to voltage signals (using transducers).
NOTE: many of the oscilloscope controls can be adjusted to suit the individual performance required by the operator.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 6: oscilloscope
When using an oscilloscope:
You can determine the time and voltage value of given signal.
You can calculate the signal frequencies.
You can tell malfunction in the oscilloscope is the component is destroying the signal.
You can find out how much of the signal is DC or AC .
You can tell if there is some noise with the signal
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 7: Oscilloscope
NOTE: oscilloscopes come in many shapes and sizes, hence, beside the power supply, the basic oscilloscope has different subsystems.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 8
Now, on the screen a spot of light is formed where the electron beam strikes and leaves a glowing trail as the beam moves across the screen (fades unless traced over)
The beam passes first between one pair of vertical and then horizontal deflection plates when the voltage is applied to the vertical deflection plates this produces an electrical field between them, which deflect the electron beam either up or down similarly the electrical field in the Horizontal plates deflects the beam left or right.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 9
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 10
CRT operation:
The signal displayed on the screen passes through the calibrated attenuator.
The attenuator matches the high impedance of the scope to the low impedance of the vertical pre-amplifier; it also scales the input signal to a level that the vertical pre-amps can handle.
Then the signal is magnified by the vertical amplifier, which provides the required deflection voltage.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 11
The trigger circuit:
Trigger level: selects the voltage of which the input signal initiates a sweep.
Slope: determines whether a sweep begins on the positive or negative ongoing slope of the wave form.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 12
The horizontal deflection plates provide a similar action where its input maybe switched between two plates of inputs:
External input (x-y)
internal input: (time-base0generator) or (sweep generator)The circuit initiating the sweep is called the trigger circuit.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 13
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 14
The heater cathode emits electrons. They are accelerated to the first accelerating anode when the amount of the cathode current controls the intensity of the spot.
The beam is focused and then sent to be given some additional energy by the 2nd accelerating anode.
Focusing the beam prevents the electrons from being diverged and producing an ill-defined spot on the phosphoric screen.
The electron beam is focused with an electrostatic lens.
This lens requires three elements with the center elements at a lower potential that the two outer elements.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 15
Oscilloscope screens:
For the inner surface of the screen,
It is phosphoric which has the property of emitting light when stimulated by radiation (kinetic energy), this property is referred to as fluorescence.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 16
The screen (phosphor) can continue the emission of light after cutting off the source; this property is known as phosphor sense.
The time of continuing emission of light is referred to as persistence of phosphor.
The persistence of phosphor is measured in terms of the time required for the image to decay to ascertain percentage (10%) of the original light output.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 17
The intensity of the image on the screen is known as “luminance”, which depends on:
The number of electrons strikes the screen/second.
energy with the electrons, which depends on the accelerated voltage.
The physical characteristics of the phosphor screen .
(in general ,phosphor (p31)) is known to be the best for general purpose viewing since it has high luminance and medium persistence.
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College