## Slide 1
4 October 2018
By : Firas AL Assadi / AL Mansour University College
<number>
Al Mansour University College
Computer Technologies Engineering Department
Second Class
Year 2018 - 2019
Instruments and Measurements Lectures
by :
Firas Al Assadi

## Slide 2
<number>
Quantity Symbol Definition Unit of Unit
measure Symbol
Current I Measure of electron flow Ampere A
Voltage E or V Force that causes electrons to flow Volts V
Resistance R Opposition to flow of electrons Ohms Ω
Power P Heat dissipated in a circuit Watts W
Capacitance C Storage capacity of a capacitor Farads f
Inductance L Storage capacity of an inductor Henries H
Reactance X Opposition to current by L or C Ohms Ω
Impedance Z Opposition to AC circuit current Ohms Ω
Frequency f Number of cycles per second Hertz Hz
Time t Time elapsed or between pulses Seconds s
Electrical Units of Measure
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 3
<number>
Engineering Notation
  Engineering Notation is a shorthand method of representing large and small numbers
  Examples: 1,000 meters = 1 kilometer
  12,000 meters = 12 kilometers
  28,400,000 Hz = 28.4 MHz (megahertz)
  0.00025 A = 25 milliamps
  0.0000025 f = 2.5 microfarads
  0.095 s = 95 milliseconds
Engineering Notation
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 4
ENGINEERING NOTATION CHART
CONVERSION FACTORS
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College
Notes: <number>

## Slide 5
To convert a number "to" engineering notation
Divide the number by the conversion factor for desired prefix
Convert 5860 Hz to kHz
Use Calculator to Convert
Kilo = 1,000 or 103
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 6
To convert a number "to" engineering notation
Divide the number by the conversion factor for desired prefix
Convert 84,450,000 W to MW
Use Calculator to Convert
mega = 1,000,000 or 106
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 7
To convert a number "to" engineering notation
Divide the number by the conversion factor for desired prefix
Convert 0.00346 A to mA
Use Calculator to Convert
milli = 0.001 or 10-3
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 8
To convert a number "from" engineering notation
Multiply the number by the conversion factor indicated
Convert 5.86 kHz to Hz
5.860 kHz = 5860 Hz
Use Calculator to Convert
Kilo = 1,000 or 103
Hz
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 9
(84.5) MW (x) (6) (10X ) (=) 84,450,000 W
84.5 MW x 1,000,000 = 84,450,000 W
To convert a number "from" engineering notation
Multiply the number by the conversion factor indicated
Convert 84.45 MW to W
84.5 MW = 84,450,000 W
Use Calculator to Convert
mega = 1,000,000 or 106
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 10
(3.45) mA (x) (-3) (10X ) (=) .00346 A
3.45 mA x 0.001 = .00346 A
To convert a number "from" engineering notation
Multiply the number by the conversion factor indicated
Convert 3.46 mA to A
3.45 mA= .00346 A
Use Calculator to Convert
milli = 0.001 or 10-3
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 11
<number>
Check Your Understanding
Complete the following
- 0.750 A = ________________ mA
- 0.20 mA = ________________ A
- 1,550 W = ________________ kW
- 330 kV = ________________ V
- 112 μF = ________________ F
- 12,550,000 Ω = _________________ M Ω
- 0.000000456 F = _________________ nF
- 222 kΩ = _________________ Ω
Engineering Notation
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College

## Slide 12
<number>
Check Your Understanding
Complete the following
- 0.750 A = ________________ mA
- 0.20 mA = ________________ A
- 1,550 W = ________________ kW
- 330 kV = ________________ V
- 112 μF = ________________ F
- 12,550,000 Ω = _________________ M Ω
- 0.000000456 F = _________________ nF
- 222 kΩ = _________________ Ω
750
0.0002
1.55
330,000
0.000,112
12.55
456
222,000
÷ .001
÷ 1,000
÷ 1,000,000
÷ .000,000,001
x .001
x 1,000
x .000,000
x 1,000
Engineering Notation
4 October 2018
<number>
By : Firas AL Assadi / AL Mansour University College